TIRHUT DUGDH UTPADAK SAHKARI SANGH LTD., MUZAFFARPUR

Annexure 1

Specifications of Drilling of Tubewell by RIG Machine Size – 12” x 8” with PVC Casing Pipe at At Sitamarhi Dairy Campus, Sitamarhi

Development of Tube well (Erection)

- 1 job of Transportation of Boring Equipment Machine tools etc, including erection and dismantling and transporting back after completion of job.

- 1 job of Construction of Pit 15 x 15 x 6 for storing water required for tube well drilling purpose.

- 100 Meters of Labour charges for boring of 450mm dia bore hole through any type of soil boring is to be done by reverse/direct circulation rotary system including labor for boring and withdrawing all drill and drill bit.

- 96 Meters of Labour charges for lowering tube well pipe. Including fixing of gravel.

- 1 job of Development charges of Tube well by Air compressor till sand free dischargetion Max 8 Hours.

- 1 job of Formation & sample collection for preparation of assembly for tube well.

- 1 job of Cost of earth filling form G.L. to 6 Meters below the G.L. around the bore well.

- 1 job of Installation and commissioning charges.

Supply & Installation of 7.5 KW Submersible Pump set Liquid to be Handed – Cleaned Cold Water free from Sand & Acid. Well Diameter – 150mm or above, Out Let Size – 80mm (3”), Supply Voltage – 400 volt +10%, Cable Size – 2 x 3 x 2.5 Sq.mm.

- 1 No. of Supply of Pump set with 3 Meters cable with total  head 49 Meters to 55 Meters Discharge capacity 36000 L/Hr to 30000 L/Hr with 6 No of stage and motor rating 7.5 KW/10HP.

- 2 no. of Supply of Supporting Clamp 3” dia.

- 80 Meter of Supply of Extra cable  Size – 1 x 3 x 2.5 Sq.mm.

- 1 no. of Supply of Control Panel (L&T or BCH Make).

- 80 Feet of Supply of 3” dia GI B Class pipe in 3 Meters length both end threaded and one end socketed.

- 1 no. of Supply of 3” dia G.I. Bend.

- 1 no. of Supply of 3” Gate Valve ISI Mark.

- 36 Meters of Supply of 12” dia CM Grade UPVC ISI mark pipe wall thickness 10mm as per IS 12818: 1992 (ORIPLAST/Jain Arrigation).

- 80 Meters of Supply of 8” dia CM Grade UPVC ISI make pipe wall thickness 10mm as per IS 12818: 1992 (ORIPLAST/Jain Arrigation/Utkarsh).

- 80 Meters of Supply of 8” dia CM Grade UPVC ISI make pipe wall thickness 7.5mm as per IS 12818: 1992 (ORIPLAST/Jain Arrigation/Utkarsh).

- 01 job of Small fitting like well cap. Well plug centre guide. M.S. rings etc.

- 36 cum of Supply of Doderma Origin Gravel.